Drill Press

Rules for use:

- Always wear safety glasses

- Do not operate while wearing jewelry or loose long sleeves or hair

- Always keep hands well clear of the bit

- Never drill with any part of your body in the path of the drill bit

- Keep your eyes on the drill until the bit has stopped spinning

Procedures for use:

- Select the proper drill bit. The Tech Director will show you where the bits are

- Chuck the drill bit. Remove the bit that is in the drill by inserting the chuck key into the hole in the chuck and turning CCW

- Insert the correct bit and tighten the chuck by turning the key clockwise.  REMOVE THE KEY FROM THE CHUCK

- Adjust the drill table height and position so the drill bit just goes through the hole in the table when in the full down position (or use a backing block if using a bit too big for the hole).

- Clamp or brace your work securely in place: A SPINNING PIECE OF WOOD OR METAL CAN CAUSE SEVERE HARM

- Check the bit. If it is chipped or worn, see the Tech Director for a new one.

- Set the drill speed, if necessary, by adjusting the drive belt on the pulleys (fast for wood, slow for metal). Make sure the drill is unplugged when changing the belt

- Turn the light on

- Line up the bit with your mark on the material to be drilled

- Turn on the drill motor

- Lower the drill into the material using the capstan lever; don’t use excessive force

- When you get close to drilling all the way through the wood, back off a little on the downward pressure. This will ensure a cleaner hole on the other side of the wood

- If you are drilling metal, use a lubricant (twist bit only – no spade bits for metal)

Remember, if you don’t feel comfortable with something – DON’T DO IT!

The Drill Press is not a toy. Treat it with respect.

This student has been trained in the proper use of the Drill Press.

Tech Director_________________________________________________

Date______/______/______

I understand the above rules, and will follow them at all times.

Student’s Signature____________________________________________

Date______/______/______

I understand my child has been properly trained on the use of the Drill, and give my permission for him/her to use it under the above conditions.

Parent’s Signature____________________________________________

Date______/______/______